## Slide 1: Construction Pathway
Student Production Classes

## Slide 2: Using classes together
Construction
Furniture and cabinet making
Cad / Technical drawing

## Slide 3: Project Based
Research community opportunities;
Lyons City hall
Nickerson City Hall
309 School District - Ticket Booth- Cafeteria remodel
Sports Posters - Senior posters & group photos

## Slide 4: Lyons City Hall
Judges Table
New building - needed a moveable judges table for new community / multipurpose room.
Research old building and new building needs - Field trip

## Slide 5
Initial Sketches
Rough dimensions
Cardboard mockup

## Slide 8: Cad Drawings

## Slide 9: Inventor Software

## Slide 10: Break production into manageable Parts
Figure material needs and send order- 6/4 walnut
Pick a project manager or you be the manager.
Cut rough pieces for Gluing. Check measurements. two students together. I send the cut list to them.
Had 1 student set up and cut raised panels.
Set teams to rough sand.
Collect all parts labed

## Slide 18: Nickerson City hall conference table
Same process - Field trip - rough dimensions - drawings - approval- order material - Production - delivery.

## Slide 19: Cafeteria remodel
Upon principal request - Budget set @ 6k.
Submitted proposal to Board for final approval.
Submitted plans 3D print and budget outline.

## Slide 21: Booth drawings on-line

## Slide 23: Butcher Block Tables
Had students mass produce;
First step - select from 1 1/2” material precut.
Make 6 rows 49” long
Plane and sand to appropriate thickness
Glue together 6 rows
Glue together 3 rows of 6 now approx 18” wide x 49” long
Plane 18” pieces to 1 1/4”, match and glue for 30” width
Sand, Sand, Sand, cut to size, router edges, sand
Pour epoxy resin (Bar coat) 2 gallons

## Slide 26: Half wall divider

## Slide 27: 4 Top Tables Reclaimed Gym Floor

## Slide 28: 32 Foot Bar height Table

## Slide 30: Park Benches

## Slide 32: Cribbage boards

## Slide 33: Ticket Booth
Design in Cad class with Revit and Chief Architect
Get specs from client
Offer several size sheds
Final approval of Drawings - order material
Teach all basic wall, floor, ceiling roof, door, window construction.

## Slide 35: Pep Band Guitar

## Slide 36: Curved stair case

## Slide 37: Chess Table CNC